## Slide 1
TEAM PROMAX’s PITCH DECK
WATTWISE: SOLAR
WATTWISE SPLITS THAT FIT
A FORECAST-LED LOCAL SOLAR ENERGY ALLOCATION ENGINE
SIME DARBY HACKATHON: TOWNSHIP OF TOMORROW
Notes: Slide 1 of the corrected WattWise pitch deck.

## Slide 2
TEAM PROMAX:
01 TEAM LEAD
SHERI ANNE CHONG TING TING · LEAD, FULL-STACK UNIVERSITY OF SOUTHAMPTON MALAYSIA (UOSM) satc1g24@soton.ac.uk 019-807 2503
02 MEMBERS
ONG HUI MIN · UI/UX DEVELOPER, RESEARCH UOSM · hmo1e25@soton.ac.uk
JESS LAU XI EN · UI/UX DESIGNER, DEVELOPER UOSM · xel1n24@soton.ac.uk
LIM POH SHIU · DATA ANALYST, QA UOSM ·psl1e25@soton.ac.uk
Notes: Slide 2 of the corrected WattWise pitch deck.

## Slide 3
1) PROBLEM STATEMENT
CREAM makes SDP pre-allocate each buyer's share of solar four months ahead.
120
days
Each buyer's share is filed in writing before the month starts, before its real demand is known.
9
sen/kWh
Access charge still paid by SDP to release solar a buyer didn’t use.
6%
of solar given away
Median waste of 6% under a fixed yearly split. One buyer pair in ten wastes 16% or more.
CREAM Guidelines 9.9, 9.10(e), 13.2 (Energy Commission, 2025; Skrine, 2025). Replay on real meters, 407 buyer pairs (Miller et al., 2020; WattWise, 2026).

## Slide 4
2) TARGET USER(S)
Who has the problem today, and what WattWise changes
01
CREAM aggregators
TODAY
SDP files every buyer's share 120 days ahead
WITH WATTWISE
Each split is sized to the buyer's predicted use.
02
Elmina homeowners
TODAY
Fixed splits waste solar, so SDP has limited room to add more roofs.
WITH WATTWISE
Up to 20% more homes can lease their roofs at no extra waste (modelled).
03
CREAM buyers
TODAY
Innovation Park today; a school, petrol stations and commercial hubs have shown interest
WITH WATTWISE
Each share comes from the buyer's own meters.
Buyer interest: The Malaysian Reserve (2025). Waste figures: median of 407 real buyer pairs (WattWise, 2026).

## Slide 5
3) OUR SOLUTION: WATTWISE
A software layer that replaces a fixed yearly guess with a monthly plan.
ESTIMATE
Each buyer's use, from its own meter history
ALLOCATE
Share sized to the estimate; a slice held back for a fallback buyer, NEDA
(New Enhanced Dispatch Arrangement)
FILE
Stamped with its 120-day notice date
LEARN
Each month checked against real use
THE RULE ANYONE CAN CHECK BY HAND
estimate = same month last year × (1 + trend)
No weather, no machine learning. Replay and rules: 02 Scheduler Module/replay.py (WattWise, 2026).

## Slide 6
4) INNOVATION & DIFFERENTIATION
What gives WattWise a new approach?
Makes & stores solar
Manages one building
Signs up roofs
Plans CREAM shares
Solarvest · GSPARX · Plus Xnergy
✓
–
–
–
Schneider Electric · Tanand
–
✓
–
–
Bright Energy · GSPARX
–
–
✓
–
WATTWISE
✓
WattWise works with these players inside the CREAM ecosystem, not against them.
Company roles summarised from their public descriptions; not independently verified.

## Slide 7
5) HOW IT WORKS
Theme: Planet · Smart energy efficiency
1
READ
3 files in
meter readings · past splits · solar output
2
ESTIMATE
120 days ahead
same month last year × trend
3
ALLOCATE
share + hold-back
2% of solar held back for NEDA
4
FILE
notice-stamped
SDP files with the Energy Commission
5
LEARN
after TNB bills
suggested vs filed vs actual
Result: solar given away drops from 6.05% to 1.34% (median, 407 buyer pairs).

## Slide 8
6) IMPACT
Less solar is thrown away
Chart: 
| Fixed yearly split | Copy last year | WattWise
Solar given away, % of the year | 6.05 | 1.95 | 1.34
Median share of the year's solar given away from 407 real buyer pairs
Real meters from 821 buildings (Miller et al., 2020) with rooftop solar at Elmina (European Commission JRC, 2022). Re-run it yourself in the testing suite.
78%
less solar given away than a fixed split
99.8%
of 407 real buyer pairs: WattWise gives away less than a fixed split
RM108k–265k
a year more at 6,000 homes, with room for about 20% more roofs (modelled)

## Slide 9
6) IMPACT
What WattWise adds to a 6,000-home scheme (modelled)
Chart: 
| 20 sen/kWh | 25 sen/kWh | 30 sen/kWh
Extra income, RM thousand a year | 265 | 184 | 108
Extra gross income a year vs a fixed split, by assumed CREAM price
RM108k–265k
a year more than a fixed yearly split
1.4%–6.6%
of the scheme's total yearly income (RM4.0M–7.9M)
6,000 homes (≈41,000 MWh a year), 2 buyers assumed. Before roof-lease payments, costs and tax.
Modelled; the CREAM price is private (assumed 20–30 sen/kWh). Scheme income is after the 9 sen grid access charge. Below 17 sen, selling to NEDA beats selling to a buyer.

## Slide 10
7) FEASIBILITY
A working prototype, tested on real meters
821
real buildings tested
99.8%
of buyer pairs give away less than a fixed split
0
hardware, no grid integration
Try the testing suite: re-run every number
Operator app prototype (screenshot). Fits SDP's digital energy services strategy (Sime Darby Property, 2026a).

## Slide 11
7) IMPLEMENTATION
How WattWise enters SDP's pipeline
01
Shadow pilot
3 months, free. SDP shares 3 files
02
Verify
Suggested vs filed vs billed
03
Live at Elmina
WattWise suggests; SDP still files
04
Scale
Monthly runs for each new buyer
05
Expand
Any approved CREAM aggregator
The first shadow report is back within a day (planned).
Build to pilot: ~4–6 weeks
Estimate. Prototype works; left: SDP file import, notice export, security review
Upkeep: near zero
No hardware, no model to retrain; only update rates if the Energy Commission changes them

## Slide 12
7) VISUAL CONCEPT
Explore the working prototype
Operator app: deadlines, estimate, notice
Testing suite: every claim, re-runnable
OPEN THE LIVE DASHBOARD
OPEN THE TESTING SUITE
Code and data: github.com/ttc-099/Wattwise

## Slide 13
8) WHY WE SHOULD WIN
Notes: Slide 12 of the corrected WattWise pitch deck.

## Slide 14
FROM TEAM PROMAX,
THANK YOU
FOR YOUR TIME!
Completed: 23 Oct 2026
Notes: Slide 13 of the corrected WattWise pitch deck.

## Slide 15
APPENDIX A: DOES IT REALLY REDUCE SOLAR GIVEAWAY?
Median share of the year's solar given away
Chart: 
| 1 buyer (821 cases) | 2 buyers (407) | 2 buyers, humid Texas site (42)
Fixed split | 5.98 | 6.05 | 3.83
Copy last year | 1.49 | 1.95 | 1.28
WattWise | 0.95 | 1.34 | 0.85
Fixed split 6.05% → WattWise 1.34% for buyer pairs.
Test it yourself
Real meters, 821 buildings (Miller et al., 2020); rooftop solar at Elmina (European Commission JRC, 2022); WattWise (2026).

## Slide 16
APPENDIX B: HOW MUCH INCOME DOES IT ADD FOR SDP?
Extra gross scheme income a year, by assumed CREAM price
Chart: 
| 20 sen/kWh | 25 sen/kWh | 30 sen/kWh
Elmina's modelled size (1,368 roofs) | 60 | 42 | 25
SDP's 6,000-home target | 265 | 184 | 108
Modest and price-dependent; roof-lease terms are SDP's private deal.
Test it yourself
Modelled, 2 buyers assumed. Before roof-lease payments, costs and tax. At 15 sen the gain would be larger, but 15 sen is below the 17 sen NEDA break-even.

## Slide 17
APPENDIX C: WILL THERE REALLY BE SPACE FOR 20% MORE CREAM CONTRIBUTORS?
Solar given away when the solar pool is built larger
Chart: 
| Today's size (1.0×) | 10% larger (1.1×) | 20% larger (1.2×)
Fixed split | 6.05 | 11.58 | 17.55
WattWise | 1.34 | 1.88 | 2.17
Still below today's fixed split, but ~76% of the extra solar sells via NEDA at 8 sen.
Test it yourself
Feeder limits (2 MWp each), roof availability and lease take-up are not modelled (WattWise, 2026).

## Slide 18
APPENDIX D: DYNAMIC SPLITTING WORKS BETTER THAN FIXED ONES?
Share of cases where WattWise gives away less
Chart: 
| Less than a fixed split | Less than copying last year
1 buyer (821 cases) | 98.5 | 77.2
2 buyers (407) | 99.8 | 83.3
Beats fixed in almost every case; above ~20 sen, copying last year earns slightly more.
Test it yourself
Real meters, 821 buildings (Miller et al., 2020); WattWise (2026).

## Slide 19
APPENDIX E: REFERENCES
Energy Commission (2025) Guidelines for Community Renewable Energy Aggregation Mechanism (CREAM), GP/ST/No.55/2025. Putrajaya: Suruhanjaya Tenaga.
European Commission Joint Research Centre (2022) Photovoltaic Geographical Information System (PVGIS) 5.2. https://re.jrc.ec.europa.eu/pvg_tools/
Miller, C. et al. (2020) 'The Building Data Genome Project 2', Scientific Data, 7, 368. https://doi.org/10.1038/s41597-020-00712-x
Sime Darby Property (2026a) Integrated Annual Report 2025. Sime Darby Property (2026b) Sustainability Report 2025.
Skrine (2025) Energy Commission issues guidelines for Malaysia's CREAM [Legal alert]. April.
The Malaysian Reserve (2025) 'Sime Darby Property, TNB launch pilot solar project under CREAM to power homes, industries', 26 September.
WattWise (2026) WattWise code and results. https://github.com/ttc-099/Wattwise. Every figure is rebuilt by python replay.py in 02 Scheduler Module.
References in the testing suite